## Slide 1
Lecture outline . . .
Sources of Uncertainty
Representing Uncertainty
Calculating Uncertainty
Sampling Uncertainty
Summarizing Over Realizations
Uncertainty Summary
Michael Pyrcz, The University of Texas at Austin
Daytum +2 Course Uncertainty

## Slide 2
Lecture outline . . .
Sources of Uncertainty
Michael Pyrcz, The University of Texas at Austin
Daytum +2 Course Uncertainty

## Slide 3: Uncertainty What is uncertainty?
u3
u1
u2
u4
u6
u7
u5
Stationary domain, samples at locations, u1-7
Property of Interest
PDF
u0
?
?
Uncertainty is not an intrinsic property of the subsurface.
At every location (uα) within the volume of interest the true properties could be measured if we had access (facies, porosity etc.).
Uncertainty is a function of our ignorance, our inability to observed and measure the subsurface with the coverage and scale required to support our scientific questions and decision making.
sparsity of sample data + heterogeneity = uncertainty
If the subsurface was homogeneous, with a few measurements uncertainty would be reduced and estimates resolved to a sufficient degree of exactitude.

## Slide 4: Types of Uncertainty
Measurement / Interpretation Error.
  Formation evaluation – tool tolerance, calibration error, approximations / assumptions
  Interpreter experience and prior model / assumptions
  How to integrate it?
    Indicator method code as soft inputs
    Multiple data realizations in design of experiments
Depth (m)
100
90
80
70
60
50
40
30
20
10
0
Gamma Ray
0
200
Example well log.

## Slide 5
Spatial Uncertainty
  Uncertainty due to spatial offset from sampled locations
  Integrate through multiple local realizations and scenarios
Types of Uncertainty

## Slide 6
Parameter Uncertainty
  Uncertainty in the input statistics to constrain the model area
  E.g. global reference porosity distribution for simulation
  Formulate distribution scenarios and bootstrap realizations
Distribution of Variogram Ranges
(Pyrcz et al., 2006)
Trend Uncertainty (Villalba and Deutsch., 2010)
Types of Uncertainty

## Slide 7
Lecture outline . . .
Representing Uncertainty
Michael Pyrcz, The University of Texas at Austin
Daytum +2 Course Uncertainty

## Slide 8
Property of Interest
PDF Z(u0)
?
z1(u0)
zn(u0)
Random
Variable
Multiple
Outcomes
Random Variables and Functions: A random variable is a property at a location (uα) that can take on multiple possible outcomes. This is represented by a probability density function (PDF).
Z(u1)
Z(u2)
Z(u3)
Z(u4)
Multiple Joint Outcomes Multiple Models
If we take a set of random variables at all locations of interest and we impart the correct spatial continuity between them then we have a random function. Each outcome from the random function is a potential model of the subsurface.
How Do We Represent Uncertainty?

## Slide 9
Using Multiple Models: We represent uncertainty with multiple models.
Scenarios: when the input decisions and parameters are changed
Captures interpretation and data uncertainty.
Realizations: when the input decisions and parameters are held constant and only the random number seed is changed
Captures spatial uncertainty.
Working With Multiple Models: It is generally not appropriate to analyze a single or few scenarios and realizations.
Use all the models all the time applied to the transfer function
(e.g. volumetric calculation, contaminant transport, ore grade scale up, flow simulation etc.).
How Do We Represent Uncertainty?

## Slide 10
We have a PDF / CDF of a measure over a volume: therefore our measures of spread / dispersion are our measures of uncertainty.
Var
Variance
Dispersion Variance
Entropy
Expected squared difference from mean.
Generalized variance accounting scale
and heterogeneity.
Measure of uncertainty for categorical
Variables.
Discrete distribution
1
2
3
1
2
3
Discrete distribution
1
2
3
1
2
3
maximum
entropy
minimum
entropy
How Do We Represent Uncertainty?

## Slide 11
Variance is partitioned between trend, deterministic, known and residual, stochastic, unknown.
Total variance = Deterministic / Known + Stochastic / Unknown
2 = t2 + r2 + 2 Ct,r (0)
Variance
Components
Variance
Variance
s2trend
s2residual
s2residual
s2trend
Variance Partitions
0
How Do We Represent Uncertainty?

## Slide 12
Variance is partitioned spatially with variogram features.
(if = 1)
For one neighboring data:
?
1
0
Nested structures each describe
spatial uncertainty components.
k2 = 2nugget + 2spherical + 2trend
nugget
spherical
trend
nugget
spherical
trend
nugget
spherical
trend
Simple Kriging Est. Var.
nugget + spherical + trend
How Do We Represent Uncertainty?

## Slide 13
Discrete Cases
  At times it is NOT possible to represent uncertainty as a continuous distribution.
  Discrete scenarios are required
    Porosity compaction trend - yes or no.
    Channelized or lobe uncertainty
How Do We Represent Uncertainty?

## Slide 14
Ergodic fluctuations – Can’t leave uncertainty to the algorithm!
  In the “old days” ergodic fluctuations were treated as a comprehensive uncertainty model in input statistics.
  Function of variogram range, data conditioning and size of model area.
  Can be predicted:
V
v
  Does not completely account for uncertainty in inferring input statistics.
  We must take ownership of our inputs and associated uncertainty models.
Generalize Variance
Definition
Fluctuations in
Variogram
How Do We Represent Uncertainty?

## Slide 15
Lecture outline . . .
Calculating Uncertainty
Michael Pyrcz, The University of Texas at Austin
Daytum +2 Course Uncertainty

## Slide 16: How is Uncertainty Calculated?
Simple example:
  Uncertainty in porosity estimate at location u1.
  Global Uncertainty from Scenario: Depositional Setting Deepwater Lobe
  Local Uncertainty given Trend Model
mglobal,2global (CaseLobe)
Porosity(u1)
mtrend(u1), 2residual(u1)
2residual (u1) = 2global (u1) - 2trend (u1)
trend

## Slide 17
Simple example:
  Uncertainty in porosity estimate at location u1.
  Local Uncertainty given Trend Model and Conditioning Data
  Uncertainty at u1 for porosity given CaseLobe, trend model and conditioning data.
Porosity(u1)
mtrend | data(u1), 2residual | data(u1)
2residual | data (u1) ~ 2residual (u1) – C(h)
trend
1
2residual | data (u1) = k2
mtrend | data(u1) = Z*
How is Uncertainty Calculated?

## Slide 18
Sample uncertainty through modeling scenarios and realizations:
  We can ask any question of the model by considering all scenarios and realizations jointly.
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1,…,L realizations (all inputs the same)
1,…,L realizations (all inputs the same)
Scenario 1
Scenario 2
1
2
3
4
5
6
7
1,…,L realizations (all inputs the same)
Scenario 3
How is Uncertainty Calculated?

## Slide 19
Modeling Subsurface Uncertainty Without Scenarios
Implicitly assume perfect knowledge of:
1
2
3
4
5
6
7
1,…,L realizations (all the same inputs)
Scenario 1
Porosity
Univariate
Distributions
mean porosity - results in reduced volumetric uncertainty
Lag Distance (h)
Spatial
Continuity
spatial heterogeneity - results in reduced recovery uncertainty
Porosity
Bivariate
Distributions
bivariate relationships - results in reduced local uncertainty and recovery uncertainty
g
Permeability
Porosity
Primary and
Secondary Data
conditioning data - results in reduced local uncertainty
Relying on ergodic fluctuations to characterize uncertainty in the input statistics.
How is Uncertainty Calculated?

## Slide 20
Working without realizations?:
  Implicitly assume perfect knowledge:
1
2
3
4
5
6
7
Scenario 1
Spatial Uncertainty
Spatially, away from data.
Freeze stochastic islands
away from data!
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Scenario 2
Scenario 3
1
2
3
4
5
6
7
H
L
Porosity Output Distribution
Input Statistic
Fluctuations
Porosity Realization
Ergodic fluctuations from target statistics.
Response Surface
Response
Surface
Ergodic fluctuations transfer to response surface creating
additional undulations.
Var1
Var2
How is Uncertainty Calculated?

## Slide 21
Uncertainty Space is Vast!
  Consider typical design
  Consider there are typically are around 10 or more uncertain variables.
    310 = 59,049 scenarios x 10 realizations of each scenario = 590,490 models
    Variable screening is important!
    3 level may still poor sampling
mporosity
2permeability
3 level design, 2 variables
levelvar = 9 scenarios
Recovery
Factor
Univariate
Response
2permeability
Fit
Model
How is Uncertainty Calculated?

## Slide 22
We have represented the “uncertainty model” through scenarios and realizations:
  We can ask any question of the model by considering all scenarios and realizations jointly.
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Porosity(u1) = F(Φ; u1)
What is the uncertainty in porosity at location u1?
How is Uncertainty Calculated?

## Slide 23
We have represented the “uncertainty model” through scenarios and realizations:
  We can ask any question of the model by considering all scenarios and realizations jointly.
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
mporosity(v) = F(Φ; v)
What is the uncertainty in average porosity over volume, v?
How is Uncertainty Calculated?

## Slide 24
We have represented the “uncertainty model” through scenarios and realizations:
  We can ask any question of the model by considering all scenarios and realizations jointly.
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
RF(1-3) = F(RF; 1-3)
What is the uncertainty in the recovery factor between Inj1 and Prod3?
How is Uncertainty Calculated?

## Slide 25
We have represented the “uncertainty model” through scenarios and realizations:
  Models could be ranked as Pxx for a specific question.
  But for every new question, the calculation of rank must be RERUN!
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
RF(1-3) = F(RF; 1-3)
Why would a single model be the P90 for all of these questions?
mporosity(v) = F(Φ; v)
Porosity(u1) = F(Φ; u1)
How is Uncertainty Calculated?

## Slide 26
Lecture outline . . .
Sampling Uncertainty
Daytum +2 Course Uncertainty

## Slide 27: Sampling the Uncertainty Space
Sampling the Uncertainty Space
Generally models are treated as equiprobably
Equal-likely to be drawn realizations of the subsurface
We are attempting to sample model the decision criteria CDF
Model 1
Model 2
Model M
Decision Criteria
Model 3
Decision
Criteria
CDF

## Slide 28
Challenges:
1. Sampling a Vast
Uncertainty Space
scenarios
realizations
Realizations
Scenario 1
Scenario 2
Scenario S
Scenarios
model choices /
parameters
levels
Transfer Function
Decision Criteria
2. Expensive Transfer Function
Sampling the Uncertainty Space

## Slide 29: Response Surfaces
Even with full combinatorial sampling we have only sampled quite a limited combination of possible parameters:
Consider this 2 parameters, 3 level model with exhaustive sampling
We have only sampled this configuration of the joint distribution!
Recall curse of dimensionality – this is poor coverage as the dimension increases
mporosity
2permeability
3 level design, 2 variables
= 9 scenarios
Recover Factor

## Slide 30
A response surface is modeled to fill in, improve coverage
Fit a hyperdimensional model to the samples of the decision criteria
Assume smooth response behavior and limited extrapolation
The Monte Carlo sample from the response surface over a complete range of the predictor variables
mporosity
2permeability
3 level design, 2 variables
= 9 scenarios
Response Surfaces

## Slide 31
A response surface is modeled to fill in, improve coverage
The Monte Carlo sample from the response surface over a complete distribution of the predictor range.
mporosity Realization
2permeability Realization
2permeability
Recover Factor Realization
Response Surfaces

## Slide 32: Sampling Designs
There are a Variety of Designs for Sampling This Uncertainty Space
Full Combinatorial
  All of the possible combinations over parameters and levels,
  Often not practical for typical problems
Optimal Designs, Set of Experimental Designs
  D-optimal – maximize the determinant of the information matrix
  C-optimal – minimize the variance of the best linear unbiased estimator
Placket-Burman
  Direct dependence (response to predictors) without predictor to predictor interdependence
Reduced designs are often used for first step of variable screening

## Slide 33
A Short Cut, Model Ranking
Use a fast proxy for the transfer function to assign a rank estimate to each model
Sorting models from P00 to P100
Model 1
Model 2
Model M
Decision Criteria
Model 3
Decision
Criteria
CDF
Rank Error
Ranking Models

## Slide 34
Model Ranking
Identify critical percentiles, P10, P50 and P90 are common
Apply expensive transfer function only to these models
Model 13
Model 729
Decision Criteria
Decision
Criteria
CDF
Model 453
P90
P50
P10
Ranking Models

## Slide 35
Model Ranking - Limitations
Ranking inaccuracy
  the fast ranking proxy has ranking error (not a perfect proxy)
  Rank P10 may actually be P13, P15 or even P53 with a poor proxy
Quite Limited Sampling of the Decision Criteria Distribution
  Simplifying assumption of distribution shape
  Extreme tail extrapolation required
  May miss our low and high cases (essential for low-side mitigation and high-side opportunity)
Rank model labels are ‘sticky’
  Once a model is labelled as P10, must retain criteria with rank!
  Common for rank label to be incorrectly retained for other criteria
Ranking Models

## Slide 36
Common Ranking Methods
Simplified Flow Physics
  Reduce complexity, e.g. single phase, streamline-based)
Geometric Proxy / Connectivity Metrics
  E.g. local static connectivity measures for a single well (Li and Deutsch, 2008).
  , cell volume, porosity, water saturation, tortuosity, permeability
Volumetric Calculation
  E.g. Global OIP in place
Ranking Models

## Slide 37
Expert Advice is to Avoid Ranking
Apply transfer function to all the models if possible
If ranking is needed, procrastinate to the latest possible in the workflow
  Ranking could be integrated at any workflow step to reduce the number of models considered to a few representative ones
  Don’t rank on static measures and then pass only a few static models for exploring dynamic model parameters
Many modeling failures can be traced to misuse of ranking
Ranking Models

## Slide 38
Lecture outline . . .
Summarizing Over Realizations
Michael Pyrcz, The University of Texas at Austin
Daytum +2 Course Uncertainty

## Slide 39: Summarizing Uncertainty Over Multiple Realizations
Multiple Realizations
Visualizing / Communicating Uncertainty
We need practical workflows to summarize over multiple realizations
Local uncertainty maps provide measures of local uncertainty suitable to support decision making (more on this later)

## Slide 40
Method:
  Scan over all the realizations and scenarios
  Calculate the local distributions of uncertainty at each location
  Calculate statistical summary over each location and place in a map / model
1
2
3
4
5
6
7
What is a specific percentile outcome at this location?
What is the local probability of exceeding a threshold at this location?
Summarizing Uncertainty Over Multiple Realizations

## Slide 41: Local Uncertainty Example
9 Realizations of porosity

## Slide 42
We will start with the e-type and the conditional variance.
e-type is the local expectation, the average of the L realizations at location as we assume all realizations are equally likely.
conditional variance is the local variance
Local Uncertainty Example

## Slide 43
Local percentile maps are the maps with the local percentile values sampled from the local realizations
We can interpret these as follows, at a location if we have a local P10 of 14% porosity, then we have a 90% probability of an even higher porosity, the porosity at that location is surely high.
Local percentiles are very convenient to understand local uncertainty. We must NOT confuse them with a percentile model (the model that is globally ranked as a specific percentile outcome).
Local Uncertainty Example

## Slide 44: Local Uncertainty Hands-on
Realization Post-processing
Things to try:
The file is Daytum_Simulation_Postsim.ipynb
Observed the results at and away from the data.
Adjust the percentiles.
Adjust the thresholds.

## Slide 45
Lecture outline . . .
Uncertainty Summary
Michael Pyrcz, The University of Texas at Austin
Daytum +2 Course Uncertainty

## Slide 46: Uncertainty Comments
Calculating Uncertainty in a Modeling Parameter: Use Bayesian methods, spatial bootstrap etc. You must account for the volume of interest, sample data quantity and locations, and spatial continuity.
If You Know It, Put It In. Use expert geologic knowledge and data to model trends. Any variability captured in a trend model is known and is removed from the unknown, uncertain component of the model. Overfit trend will result in unrealistic certainty.
Types of Uncertainty: (1) data measurement, calibration uncertainty, (2) decisions and parameters uncertainty, and (3) spatial uncertainty in estimating away from data. Your job is to hunt for and include all significant sources of uncertainty.
Be an uncertainty detective! Discover and evaluate various sources.

## Slide 47
What about Uncertainty in the Uncertainty? Don’t go there! Use defendable choices in your uncertainty model, be conservative about what you known, document and move on.
Uncertainty Depends on Scale. It is much harder to predict a property of tea spoon vs. a house-sized volume at a location (uα) in the subsurface. Ensure that scale and heterogeneity are integrated.
You Cannot Hide From It. Ignoring uncertainty assumes certainty and is often a very extreme and dangerous assumption.
Decision Making with Uncertainty. Apply all the models to the transfer function to calculate uncertainty in subsurface outcome to support decision making in the presence of uncertainty.
Ignoring uncertainty is assuming certainty.
Uncertainty Comments

## Slide 48
Lecture outline . . .
Sources of Uncertainty
Representing Uncertainty
Calculating Uncertainty
Sampling Uncertainty
Summarizing Over Realizations
Uncertainty Summary
Michael Pyrcz, The University of Texas at Austin
Daytum +2 Course Uncertainty

## Slide 49: Uncertainty New Tools
Topic | Application to Subsurface Modeling
Sources of Uncertainty | Seek out and integrate all significant sources of uncertainty. Uncertainty in the data measures based on data realizations combined with spatial uncertainty with multiple spatial realizations.
Scenarios | Capture uncertainty in model parameters and decisions through multiple scenarios. Construction of 3 set of realizations for low, mid and high case spatial continuity models.
Calculating Uncertainty | Use bootstrap, model resampling, expert assessments, Bayesian updating etc. Use a combination of expert judgement, analogs and robust statistical methods.
Michael Pyrcz, The University of Texas at Austin