## Slide 1
Lecture outline . . .
Stationarity
Spatial Continuity
Variogram Calculation
Spatial Estimation
Introduction
Fundamental Concepts
Data Prep / Analytics
Spatial Continuity / Prediction
Multivariate Modeling
Probability
Instructor: Michael Pyrcz, the University of Texas at Austin
Machine Learning
Uncertainty Modeling
Daytum +2 Course Spatial Data Analytics

## Slide 2
Lecture outline . . .
Stationarity
Instructor: Michael Pyrcz, the University of Texas at Austin
Daytum +2 Course Spatial Data Analytics

## Slide 3: Stationarity Substituting Time for Space
Extracted Sample at Location, u1
Hole Remains at Location, u1
After Sample
Extraction
Any statistic requires replicates, repeated sampling (e.g. air or water samples from a monitoring station). In our geospatial problems repeated samples are not available at a location in the subsurface.
Instead of time, we must pool samples over space to calculate our statistics. This decision to pool is the decision of stationarity. It is the decision that the subset of the subsurface is all the “same stuff”.

## Slide 4: Stationarity Substituting Time for Space
u3
u1
u2
u4
u6
u7
u5
Stationary domain, samples at locations, u1-7
Property of Interest
Histogram
The decision of the stationary domain for sampling is an expert choice. Without it we are stuck in the “hole” and cannot calculate any statistics nor say anything about the behavior of the subsurface between the sample data.
Import License: choice to pool specific samples to evaluate a statistic.
Export License: choice of where in the subsurface this statistic is applicable.

## Slide 5: Stationarity Definition 1: Geologic
Geological Definition: e.g. ‘The rock over the stationary domain is sourced, deposited, preserved, and postdepositionally altered in a similar manner, the domain is map-able and may be used for local prediction or as information for analogous locations within the subsurface; therefore, it is useful to pool information over this expert mapped volume of the subsurface.’
Photomosaic, line drawing Punta Barrosa Formation sheet complex (Fildani et al. (2009).

## Slide 6: Stationarity Definition 2: Statistical
Statistical Definition: The metrics of interest are invariant under translation over the domain. For example, one point stationarity indicates the that histogram and associated statistics do not rely on location, u. Statistical stationarity for some common statistics:
Stationary Mean: = m,
Stationary Distribution:
Stationary Semivariogram: ,
Stationarity: What metric / statistic? Over what volume?
May be extended to any statistic of interest including, facies proportions, bivariate distributions and multiple point statistics.

## Slide 7
Lecture outline . . .
Spatial Continuity
Instructor: Michael Pyrcz, the University of Texas at Austin
Daytum +2 Course Spatial Data Analytics

## Slide 8
Simple Example
Area of interest
1 Injector and 4 producers
Porosity and permeability distributions (held constant for all cases)
1,000m
1,000m
Injector#1
Producer#1
Producer#2
Producer#3
Producer#4
Permeability (mD)
1
200
Porosity (%)
5
20
Frequency
Frequency
Motivation for Measuring Spatial Continuity

## Slide 9
Does spatial continuity of reservoir properties matter?
Consider these models of permeability
Recall – all models have the same porosity and permeability distributions
Mean, variance, P10, P90 …
Same static oil in place!
Permeability (mD)
100
1
10
Motivation for Measuring Spatial Continuity

## Slide 10
How does heterogeneity impact recovery factor?
Permeability (mD)
100
1
10
Time of Flight (PV)
1
0
0.5
Motivation for Measuring Spatial Continuity

## Slide 11
Permeability (mD)
100
1
10
Time of Flight (PV)
1
0
0.5
Motivation for Measuring Spatial Continuity
How does heterogeneity impact recovery factor?

## Slide 12
Permeability (mD)
100
1
10
Time of Flight (PV)
1
0
0.5
Motivation for Measuring Spatial Continuity
How does heterogeneity impact recovery factor?

## Slide 13
For the same reservoir property distributions a wide range of spatial continuities are possible.
Spatial continuity often impacts reservoir forecasts.
Need to be able to:
“Very Short”
Spatial Continuity
“Medium”
“Long”
“Anisotropic “
Characterize / Quantify
Impose in Reservoir Models
Spatial Continuity
Measures
Motivation for Measuring Spatial Continuity

## Slide 14
Spatial Continuity – correlation between values over distance.
  No spatial continuity – no correlation between values over distance, random values at each location in space regardless of separation distance.
  Homogenous phenomenon have perfect spatial continuity, since all values as the same (or very similar) they are correlated.
Spatial Continuity Definition

## Slide 15
We need a statistic to quantify spatial continuity!
The Semivariogram:
Function of difference over distance.
The equation:
One half the average squared difference over lag distance, , over all possible pairs of data, .
Lag Distance (h), meters in X direction
200
1000
400
600
800
u
u + h
h
Location Vector
Location Vector
Lag Vector
Variogram
Modified from Deutsch, MinE310
x
y
tail
head
tail
head
Measuring Spatial Continuity

## Slide 16: “h” Scatterplot
The variogram calculated for lag distance, , corresponds to the expected value of squared difference:
Calculate for a suite of lag distances to obtain a continuous function.

## Slide 17
Variogram – a measure of dissimilarity vs. distance. Calculated as ½ the average squared difference of values separated by a lag vector.
  The precise term is semivariogram (variogram if you remove the 1/2 ), but in practice the term variogram is used.
  The ½ is used so that the covariance function and variogram may be related directly:
  Note the correlogram is related to the covariance function as:
Variogram Definition
, h-scatter plot correlation vs. lag distance

## Slide 18
Observation #1
As distance increases, variability increase (in general).
Lag Distance (), m in x direction
200
1000
400
600
800
Semivariogram
Increasing
Variability
Increase in variability with increase in lag distance (zoomed in)
x
y
Variogram Observations

## Slide 19
Observation #2
Calculated with over all possible pairs separated by lag vector, .
The variogram:
Given the number of pairs
available N(h).
Lag Distance (), m in x direction
200
1000
400
600
800
Semivariogram
h = 100 in x direction
Scan of all possible sets of pairs (zoomed in)
h = 100
x
y
Variogram Observations

## Slide 20
Observation #3
Need to plot the sill to know the degree of correlation.
Sill is the Variance, σ2
Given stationarity of the variance and :
Covariance Function:
Given a standardized distribution :
Correlogram:
Lag Distance (), m in x direction
200
1000
Sill = No Correlation = σ2
400
600
800
Semivariogram
Correlation(h) = , if =1.0
Correlation() = 0.5
Correlation() = 0
tail
head
tail
head
h – lag scatter plots
Variogram Observations

## Slide 21
Variogram Interpretation
Observation #3
Need to plot the sill to know the degree of correlation.
Another illustration of h-scatter plot correlation vs. lag distance.
3
2
0
-1
-2
-3
-3
-2
-1
0
1
2
3
1
Tail Value
Head Value
3
2
0
-1
-2
-3
-3
-2
-1
0
1
2
3
1
Tail Value
Head Value
3
2
0
-1
-2
-3
-3
-2
-1
0
1
2
3
1
Tail Value
Head Value
1.6
0.8
0.4
0.0
0
10.0
20.0
30.0
1.2
γ
Distance
p = 0.60
p = 0.02
p = -0.47

## Slide 22
Observation #4
The lag distance at which the variogram reaches the sill is know as the range.
Lag Distance (), m in x direction
200
1000
Sill = No Correlation
400
600
800
Semivariogram
Range
Correlation() = 0
tail
head
At the range, knowing the data value at the tail provides no information about a value at the head.
Range
Well
No Information
x
y
Variogram Observations

## Slide 23
Observation #5
Sometimes there is a discontinuity in the variogram at distances less than the minimum data spacing. This is known as nugget effect.
  As a ratio of nugget / sill, is known as relative nugget effect (%)
  Modeled as a no correlation structure that at lags, , an infinitesimal distance
  Measurement error, mixing populations cause apparent nugget effect
Lag Distance (h), m in x direction
200
1000
400
600
800
Semivariogram
Nugget Effect
Variogram Observations

## Slide 24: Spatial Variability
The three maps are remarkably similar: all three have the same 50 data, same histograms and same range of correlation, and yet their spatial variability/continuity is quite different
The spatial variability/continuity depends on the detailed distribution of the petrophysical attribute (,)
The charts on the left are “variograms”
Our map-making efforts should consider the spatial variability/continuity of the variable we are mapping:
  Variability
  Uncertainty
Porosity Realizations with 3 isotropic variograms.
Distance (m)
Distance (m)
Distance (m)
X (m)
Y (m)

## Slide 25
Lecture outline . . .
Variogram Calculation
Instructor: Michael Pyrcz, the University of Texas at Austin
Daytum +2 Course Spatial Data Analytics

## Slide 26
Variogram – a measure of dissimilarity vs. distance. Calculated as ½ the average squared difference of values separated by a lag vector.
  The precise term is semivariogram (variogram if you remove the 1/2 ), but in practice the term variogram is used.
  The ½ is used so that the covariance function and variogram may be related directly:
  Note the correlogram is related to the covariance function as:
Variogram Definition
, h-scatter plot correlation vs. lag distance

## Slide 27: Variogram Calculation
Consider data values separated by lag vectors (the h values)
Here are two examples of a lag vector equal to the data spacing and then twice the data spacing:

## Slide 28: Variogram Calculation
Consider data values separated by lag vectors (the h values)
Here are two examples of a lag vector equal to the data spacing and then twice the data spacing:

## Slide 29: Variogram Calculation
Pick a lag distance and calculate the variogram for that one lag distance.
Depth | N[Porosity]
0.25 | -1.37
0.5 | -2.08
0.75 | -1.67
1 | -1.16
1.25 | -0.24
1.5 | -0.36
1.75 | 0.44
2 | 0.36
2.25 | -0.02
2.5 | -0.63
2.75 | -1.26
3 | -1.03
3.25 | 0.88
3.5 | 1.51
3.75 | 1.37
4 | 0.81
4.25 | 1.21
4.5 | 0.24
4.75 | 0.99
5 | 0.49
5.25 | 0.34
5.5 | 0.07
5.75 | -0.26
6 | -0.41
6.25 | -0.14
6.5 | -1.44
6.75 | -0.75
7 | -0.78
7.25 | -0.85
7.5 | -0.92
7.75 | -0.66
8 | 0.47
8.25 | 0.85
8.5 | 0.95
8.75 | 2.35
9 | 0.69
9.25 | 1.31
9.5 | 0.66
9.75 | 0.72
10 | 0.21
The file is Variogram_Simple_Calculation.xlsx

## Slide 30: Variogram Calculation Example
Depth | N[Porosity]
0.25 | -1.37
0.5 | -2.08
0.75 | -1.67
1 | -1.16
1.25 | -0.24
1.5 | -0.36
1.75 | 0.44
2 | 0.36
2.25 | -0.02
2.5 | -0.63
2.75 | -1.26
3 | -1.03
3.25 | 0.88
3.5 | 1.51
3.75 | 1.37
4 | 0.81
4.25 | 1.21
4.5 | 0.24
4.75 | 0.99
5 | 0.49
5.25 | 0.34
5.5 | 0.07
5.75 | -0.26
6 | -0.41
6.25 | -0.14
6.5 | -1.44
6.75 | -0.75
7 | -0.78
7.25 | -0.85
7.5 | -0.92
7.75 | -0.66
8 | 0.47
8.25 | 0.85
8.5 | 0.95
8.75 | 2.35
9 | 0.69
9.25 | 1.31
9.5 | 0.66
9.75 | 0.72
10 | 0.21
Pick a lag distance and calculate the variogram for that one lag distance.
Here’s all of them:

## Slide 31: The Variogram and Covariance Function
The variogram, covariance function and correlation coefficient are equivalent tools for characterizing spatial two-point correlation (assuming stationarity):
  where:
  Stationarity entails that:
, if stationary mean
,

## Slide 32: The Variogram and Covariance Function
Must plot variance to interpret variogram:
  Positive correlation when semivariogram less than variance
  No correlation when the semivariogram is equal to the variance
  Negative correlation when the semivariogram points above variance
C(0) = s2
(h)
C(h)
0
r = 0
r > 0
r < 0
h
“lag” Distance

## Slide 33
Covariance Function – a measure of similarity vs. distance. Calculated as the average product of values separated by a lag vector centered by the square of the mean.
  The covariance function is the variogram upside down.
  We model variograms, but inside the kriging and simulation methods they are converted to covariance values for numerical convenience.
Covariance Function Definition
, if stationary mean

## Slide 34
Nugget Effect – discontinuity in the variogram at distances less than the minimum data spacing
  As a ratio of nugget / sill, is known as relative nugget effect (%)
  Measurement error, mixing populations cause apparent nugget effect
Sill – the sample variance
  Interpret spatial correlation relative to the sill, level of no correlation
Range – lag distance to reach
the sill
  Up to that distance you have
  information
  parameterization of variogram models
Variogram Components Definition
g
h
Sill
Range
Nugget
Effect

## Slide 35: Spoiler Alert
Calculate variogram with irregularly spaced data
  Search templates with parameters
Valid spatial model
  Fit with a couple different, nest (additive) spatial continuity models e.g. nugget, spherical, exponential and Gaussian
Full 3D spatial continuity model
  Model primary directions, i.e. major horizontal, minor horizontal and vertical and combine together with assumption of geometric anisotropy
We will not cover variogram modeling.
We need to practically calculate and model spatial continuity. From the available and often sparse subsurface data.

## Slide 36: Calculating Experimental Variograms
Regular spaced data:
  Specify as offsets of grid units
  Fast calculation
  Diagonal directions are awkward
Irregular spaced data:
  Nominal distance for each lag
  Distance tolerance
  Azimuth direction
  Azimuth tolerance
  Dip direction
  Dip tolerance
  Bandwidth (maximum deviation) in originally horizontal plane
  Bandwidth in originally vertical plane
Lag 2
Lag 1
Lag 4
Lag 3
Lag Tolerance
Azimuth
tolerance
Bandwidth
Azimuth
Y axis (North)
X axis (East)
Lag Distance
How do we get pairs separated by lag vector?
Image from Pyrcz and Deutsch, 2014

## Slide 37: Calculating Experimental Variograms
Example: Starting With One Lag (i.e. #4)
Start at a node, and compare value to all nodes which fall in the lag and angle tolerance.
...

## Slide 38: Calculating Experimental Variograms
...
Move to next node.

## Slide 39: Calculating Experimental Variograms
Now Repeat for All Nodes
And Repeat for All Lags
...
No correlation
Increasing
Variability
Variogram, g(h)
Lag Distance (h)

## Slide 40: Some Options
Data transformation:
  Transform a continuous variable to a Gaussian or normal distribution, for use with / consistency with Gaussian simulation methods
  Transform a categorical variable to a series of indicator variables for indicator methods and categorical to continuous for truncated Gaussian methods
Coordinate transformation:
  Variograms are calculated aligned with the stratigraphic framework
  Otherwise the spatial continuity will be underestimated
Should calculate the variogram on the variable being modeled with transforms (data and coordinates)
Calculate the variogram, as this is what we model and apply in estimation and simulation (more later).

## Slide 41: Choosing the Directions
Inspect the data and interpretations, sections, plan views, …
Azimuth angles in degrees clockwise from north
Review multiple directions before choosing a set of 3 perpendicular directions
  Omnidirectional: all directions taken together  often yields the most well-behaved variograms.
  Major horizontal direction & two perpendicular to major direction
  All anisotropy in geostatistics is geometric – three mutually orthogonal directions with ellipsoidal change in the other directions:
Image from Pyrcz and Deutsch, 2014

## Slide 42: Choosing the Lag Distances and Tolerances
Guidance for Variogram Calculation Parameters:
Lag separation distance should coincide with data spacing
Lag tolerance typically chosen to be ½ lag separation distance
  in cases of erratic variograms, may choose to overlap calculations so lag tolerance > ½ lag separation, results in more pairs.
The variogram is only valid for a distance one half of the field size: start leaving data out of calculations with larger distances
Lag 2
Lag 1
Lag 4
Lag 3
Lag Tolerance
Azimuth
tolerance
Bandwidth
Azimuth
Y axis (North)
X axis (East)
Lag Distance
Image from Pyrcz and Deutsch, 2014

## Slide 43: Spatial Calculation in Demo in Python
Experiment with Variogram Calculation:
Things to Try:
Variogram maps
Relate to the data location maps
Directional variograms
Change lag tolerance
Change lag distance
Python notebook file: GeostatsPy_spatial_continuity_directions.ipynb

## Slide 44: Spatial Continuity New Tools
Topic | Application to Subsurface Modeling
Stationarity | In the presence of multivariate relationships, must jointly model variables. Summarize with bivariate statistics, and visualize and use conditional statistics to go beyond linear measures.
Random Variables and Functions | Random variables and random functions are used to represent spatial uncertainty. Porosity at a pre-drill location has the uncertainty model based on a random variable with Gaussian mean of 15% and standard deviation of 3%.
Variogram Calculation | Calculate spatial continuity from spatial data to use for spatial prediction. From the available wells the porosity spatial continuity range is 300 m in the 030 azimuth, we have no information beyond this spacing from existing wells.

## Slide 45
Lecture outline . . .
Spatial Estimation
Instructor: Michael Pyrcz, the University of Texas at Austin
Daytum +2 Course Spatial Data Analytics

## Slide 46: Trend Modeling
We Must Start with Trend Modeling
Geostatistical spatial estimation methods make an assumption concerning stationarity
  In the presence of significant nonstationarity we would not rely 100% for spatial estimation on data + spatial continuity model
X(m)
Vsh(%)
20
5
10
15
v(u1)
v(u2)
v(u3)
v(u4)
v(u5)
What is Vsh
at location u0?
u0
Data

## Slide 47: Trend Modeling
Geostatistical spatial estimation methods will make an assumption concerning stationarity
  If we observe a trend, we should model the trend.
X(m)
Vsh(%)
20
5
10
15
v(u1)
v(u2)
v(u3)
v(u4)
v(u5)
u0

## Slide 48: Trend Modeling
Geostatistical spatial estimation methods will make an assumption concerning stationarity
  Then model the residuals.
X(m)
Residual Vsh(%)
5.0
-0.5
0
2.5
v(u1)
v(u2)
v(u3)
v(u4)
v(u5)
u0
-1.0
Model

## Slide 49: Trend Modeling
Geostatistical spatial estimation methods will make an assumption concerning stationarity
  After modeling, add the trend back to the modelled residuals
X(m)
Vsh(%)
20
5
10
15
v(u1)
v(u2)
v(u3)
v(u4)
v(u5)
u0

## Slide 50: Trend Modeling
  How bad could it be if we did not model a trend?
  Geostatistical estimation would assume stationarity and away from data we would estimate with the global mean (simple kriging)!
Model with
stationary
mean + data.
Model with
mean trend model
and residual + data.
X(m)
Vsh(%)
20
5
10
15
v(u1)
v(u2)
v(u3)
v(u4)
v(u5)
u0
X(m)
Vsh(%)
20
5
10
15
v(u1)
v(u2)
v(u3)
v(u4)
v(u5)
u0

## Slide 51: Trend Modeling
Trend Modeling
  We must identify and model
  trends / nonstationarities
Large Scale
Trend
Small Scale
Trend
Variable
of Interest
Variable
of Interest
Z variable value
x Coordinate (m)

## Slide 52: Trend Modeling
Any variance in the trend is removed from the residual:
  So if is the total variance (variability), and is the variability that is deterministically modelled, treated as known, and is the component of the variability that is treated as unknown.
  Result: the more variability explained by the trend the less variability that remains as uncertain.
if the = 0
Unknown
Residual
Known
Trend

## Slide 53: Definition Deterministic Model
Model that assumes perfect knowledge, without uncertainty
Based on knowledge of the phenomenon or trend fitting to data
Most subsurface models have a deterministic component (trend) to capture expert knowledge and to provide a stationary residual for geostatistical modeling.

## Slide 54: Trend Modeling Hands-on
File Name: Daytum_Trends_v2.ipynb
Here’s an opportunity for experiential learning with Trend Modeling.
Things to try:
Set the radius very large (50). How’s the trend model performing? Try radius very small (1).
What do you think is the best radius to fit a trend to this spatial data?

## Slide 55: Spatial Estimation
Consider the case of estimating at some unsampled location:
How would you do this given data, and
Note: z is the variable of interest (e.g. porosity etc.) and is the data locations.
x
y
1
2
3
?

## Slide 56: Spatial Estimation
Consider the case of estimating at some unsampled location:
How would you do this given data, and
Unbiasedness
Constraint
Weights sum to 1.0.
x
y
1
2
3
?
is an estimate
is the data weights
is the data values
is the global mean

## Slide 57: Spatial Estimation
Consider the case of estimating at some unsampled location:
How would you do this given data, and
In the case where
the mean is non-stationary.
Given y,
Simplified with residual, y.
x
y
1
2
3
?

## Slide 58: Spatial Estimation
Consider the case of estimating at some unsampled location:
Linear weighted, sound good. How do we get the weights?
Simplified with residual, y.
x
y
1
2
3
?

## Slide 59: Spatial Estimation
Consider the case of estimating at some unsampled location:
Linear weighted, sound good. How do we get the weights?
Equal weighted / average?
What’s wrong with that?
Equal weight
average of data
x
y
1
2
3
?

## Slide 60: Spatial Estimation
Consider the case of estimating at some unsampled location:
How do we get the weights?
Inverse distance?
What’s wrong with that?
Inverse distance to power
standardized so weights
sum to 1.0.
x
y
1
2
3
?

## Slide 61: Spatial Estimation
Consider the case of estimating at some unsampled location:
How do we get the weights?
It would be great to use weight that account for closeness (spatial correlation > distance alone), redundancy (once again with spatial correlation).
How can we do that?
x
y
1
2
3
?

## Slide 62: Spatial Estimation
Kriging Derivations Removed
The results is a very useful and interpretable linear system of equations.

## Slide 63: Simple Kriging: Some Details
There are three equations to determine the three weights:
In matrix notation: Recall that
redundancy
closeness
=
=
=
x
y
1
2
3
?
weights

## Slide 64: Properties of Simple Kriging
What Does Kriging Provide?:
Best Estimate: Minimum error estimator (just try to pick weights, you won’t bet it)
Estimation Variance: Provides a measure of the estimation (or kriging) variance (uncertainty in the estimate):
Estimation
Variance
Variance
Covariance Between
Data and Estimate Location
Kriging Weights

## Slide 65: More Properties
Exact interpolator: at data location
Kriging variance can be calculated before getting the sample information, homoscedastic!
Kriging takes into account:
  distance of the information:
  configuration of the data:
  structural continuity of the variable being considered:
The smoothing effect of kriging can be forecast – we will return to this with simulation.
Kriging theory is part of the probabilistic theory of projectors: orthogonal projection onto space of linear combinations of the n data (Hilbert space)

## Slide 66: Simple Kriging Hands-on
File Name: Daytum_Kriging.ipynb
Here’s an opportunity for experiential learning with Simple Kriging.
Things to try:
Change the indicator kriging to simple kriging from originary kriging.
Decrease the variogram range.
Increase the geometric anisotropy.

## Slide 67: Spatial Estimation New Tools
Topic | Application to Subsurface Modeling
Trend Modeling | Decompose variance into deterministic trend and stochastic residual. 30% of porosity variance is described by a linear depth trend and 70% is described by a 3D variogram model.
Kriging Estimates and Kriging Variances | Kriging provides the best estimate and a measure of estimation variance. Given a kriging estimate of 13% and kriging variance of 9% and the assumption of a Gaussian distribution we have a complete local distribution of uncertainty for pre-drill porosity.

## Slide 68: Data Analytics, Geostatistics and Machine Learning Spatial Continuity / Prediction
Lecture outline . . .
Spatial Estimation
Introduction
Fundamental Concepts
Data Prep / Analytics
Spatial Continuity / Prediction
Multivariate Modeling
Probability
Instructor: Michael Pyrcz, the University of Texas at Austin
Machine Learning
Uncertainty Modeling